## Slide 1: Lecture 13 – MOSFET 场效应晶体管-part2
Chapter 5 from Microelectronic Circuits Text by Sedra and Smith
Oxford Publishing

## Slide 2: 不同的工作区域
饱和区
非饱和区
2
不考虑沟道调制效应

## Slide 3: 如何判断工作区域（很重要！）
方法一，从物理上理解：当VG-VD > VTH 时, 漏极附近仍有沟道，MOSFET 工作在非饱和区；当VD继续增加，导致VG-VD等于或小于 VTH 时，漏极附近无沟道（沟道夹断），MOSFET进入饱和区。
方法二，从符号上理解（电路分析中最有效），要使MOSFET工作在饱和区，VD的下限为VG-VTH（参考电路图）；
方法三，记住这张图的横坐标，当VDS > VOV时，进入饱和区；
3

## Slide 4: 饱和区 还是 非饱和区?
当工作区域不确定时，我们采用本课程通用的方法：“先假设，再验证”！
4

## Slide 5
VD最低不得低于VG-VTH
注意，题目中若没有明确说明或，则不用考虑沟道调制效应
5

## Slide 6
6

## Slide 7
7

## Slide 8
8

## Slide 9: PMOS 晶体管
MOSFET 器件也可以制造在n衬底上，以空穴作载流子，这类MOSFET被称为 PMOS 晶体管，相应的，之前我们讨论的制造在p衬底上，以电子作为载流子的MOSFET被称为NMOS.
PMOS的特性与NMOS类似，只是极性相反。S电势最高
如何判断工作区：
从符号上理解（电路分析中最有效），要使PMOS工作在饱和区，VD的上限为VG + |VTH|
非饱和区
临界
饱和区
9

## Slide 10
10

## Slide 11: PMOS 方程
用绝对值表示，公式与NMOS可以统一
11

## Slide 12: 5.1.7. The p-Channel MOSFET
PMOS technology originally dominated the MOS field (over NMOS). However, as manufacturing difficulties associated with NMOS were solved, “they” took over
Q: Why is NMOS advantageous over PMOS?
  A: Because electron mobility mn is 2 – 4 times greater than hole mobility mp.
complementary MOS (CMOS) technology – is technology which allows fabrication of both N and PMOS transistors on a single chip.
12

## Slide 13: 5.1.8. Complementary MOS or CMOS
CMOS employs MOS transistors of both polarities.
Figure 5.10: Cross-section of a CMOS integrated circuit. Note that the PMOS transistor is formed in a separate n-type region, known as an n well. Another arrangement is also possible in which an n-type body is used and the n device is formed in a p well. Not shown are the connections made to the p-type body and to the n well; the latter functions as the body terminal for the p-channel device.
在p衬底上先制备一个n阱（n-well），然后在n阱里制备PMOS，在p衬底上制备NMOS，该技术称之为CMOS（Complementary MOS）.
Intel第一代CPU，4004，是使用纯NMOS技术，之后都采用了CMOS技术
13
Notes: First demonstrated by RCA for watches. They owned the technology but frittered it away by a series of management errors.

## Slide 14
Figure 5.10: Cross-section of a CMOS integrated circuit. Note that the PMOS transistor is formed in a separate n-type region, known as an n well. Another arrangement is also possible in which an n-type body is used and the n device is formed in a p well. Not shown are the connections made to the p-type body and to the n well; the latter functions as the body terminal for the p-channel device.
p-type semiconductor provides the MOS body (and allows generation of n-channel)
n-well is added to allow generation of p-channel
SiO2 is used to isolate NMOS from PMOS
14
Notes: The diode between the n-well and the p-type substrate isolates the PMOS transistor.

## Slide 15: 衬底效应
NMOS，当源极电压大于零时，因衬底始终接地，VSB会对MOSFET的阈值电压产生影响，称之为衬底效应（Body Effect）
了解就可以
15

## Slide 16: MOSFET的种类
重点理解
耗尽型：VGS=0 时已具有沟道
16

## Slide 17
17

## Slide 18: Quick Recap!
The equation used to define iD depends on relationship btw vDS and vOV.
  vDS << vOV
  vDS < vOV
  vDS >= vOV
  vDS >> vOV
（饱和区）
最重要！
18

## Slide 19: 5.2. Current-Voltage Characteristics 伏安特性，电流电压约束关系
Figure 5.11. shows an n-channel enhancement MOSFET. N沟道增强型MOSFET的电路符号
There are four terminals:
  drain (D), gate (G), body (B), and source (S).
Although, it is assumed that body and source are connected.
Figure 5.11 (a): Circuit symbol for the n-channel enhancement-type MOSFET. (b) Modified circuit symbol with an arrowhead on the source terminal to distinguish it from the drain and to indicate device polarity (i.e., n channel). (c) Simplified circuit symbol to be used when the source is connected to the body or when the effect of the body on device operation is unimportant.
19
Notes: Note that there are several different circuit symbols used for MOSFETs. The symbol used for P-Channel MOSFETs in Multisim causes much confusion.

## Slide 20: 5.2. Current-Voltage Characteristics
Although MOSFET is symmetrical device, one often designates terminals as source and drain.
Q: How does one make this designation?
  A: By polarity of voltage applied.
Arrowheads designate “normal” direction of current flow
  Note that, in part (b), we designate current as DS.
  No need to place arrow with B.
Figure 5.11 (a): Circuit symbol for the n-channel enhancement-type MOSFET. (b) Modified circuit symbol with an arrowhead on the source terminal to distinguish it from the drain and to indicate device polarity (i.e., n channel). (c) Simplified circuit symbol to be used when the source is connected to the body or when the effect of the body on device operation is unimportant.
vD is always > vS
箭头标记在S端
箭头表示电流方向
NMOS，S在下 PMOS，S在上
20
Notes: The “symmetry” is not quite true for commercially available devices due to connection from the substrate to the source. They do not wok when upside down.

## Slide 21
三个不同的工作区域
21

## Slide 22: 5.2.2. The iD-vDS Characteristics
At top of table, it shows circuit consisting of NMOS transistor and two dc supplies (vDS, vGS)
This circuit is used to demonstrate iD-vDS characteristic
  1st set vGS to desired constant
  2nd vary vDS
Two curves are shown…
  vGS < Vtn
  vGS = Vtn + vOV
22

## Slide 23
首先根据 VGS 判断器件是否 turn on
其次，再根据 VD 与 VG 的关系，判断器件是否在饱和区
若作为放大器使用，一般都需要工作在饱和区，可以先假设，再验证
23
Notes: Put a sticky at this page!

## Slide 24
24

## Slide 25
NMOS: VD最低不得低于VG-VTH
PMOS: VD最高不得高于VG+|VTH|
25

## Slide 26
Figure 5.13: The iD – vDS characteristics for an enhancement-type NMOS transistor
as vGS increases, so do the (1) saturation current and (2) beginning of the saturation region
equation (5.14)
26
Notes: Add a “Load Line” to find the Quiescent point.

## Slide 27: 5.2.2. The iD-vDS Characteristic 输出特性
Q: When MOSFET’s are employed to design amplifier, in what range will they be operated?
  A: saturation
In saturation, the drain current (iD) is…
  dependent on vGS
  independent of vDS
  理想的压控电流源！
In effect, it becomes a voltage-controlled current source.
  This is key for amplification.
Figure 5.13: The iD – vDS characteristics for an enhancement-type NMOS transistor
27

## Slide 28: 5.2.2. The iD-vGS Characteristic 转移特性
In effect, it becomes a voltage-controlled current source.
  This is key for amplification.
  Refer to (5.21).
Q: What is one problem with (5.21)?
  A: It is nonlinear w/ respect to vOV … however, this is not of concern now.
Figure 5.14: The iD-vGS characteristic of an NMOS transistor operating in the saturation region. The iD-vOV characteristic can be obtained by simply re-labeling the horizontal axis, that is, shifting the origin to the point vGS = Vtn.
28

## Slide 29: large-signal models 大信号模型
基于VDS的不同, MOSFET 有不同的大信号模型.
大信号模型~器件大范围的电压电流约束关系，往往是非线性的；小信号模型~叠加于大信号模型某一直流工作点之上的微小变化信号的模型，将非线性曲线在微小范围内线性化
饱和区，考虑沟道调制效应
非饱和区
非饱和区（VDS很小时）
29

## Slide 30
30

## Slide 31
50小于100，进入非饱和区
31

## Slide 32
32

## Slide 33: MOSFET 电路直流分析
基于 MOSFET 的“电流电压”约束关系
基于基本电路原理与分析方法
为简单起见，若无明确说明，一般我们不考虑沟道调制效应
根据有效电压VOV来分析电路，会比较方便

## Slide 34
①根据VDD，VD，ID，求RD

## Slide 35
②求RS，需要知道VS，VS可以根据VGS得到，VGS可以由VOV + VTH得到，VOV由ID决定。
③判断MOSFET的工作状态。VD > VG  饱和区

## Slide 36
① VD = VG  工作于饱和区
②

## Slide 37
①VD低于VG-VTH  工作于非饱和区
②根据VD求RD

## Slide 38
①
②
③
④
③ 假设工作在饱和区

## Slide 39
①
②
③
④
③ 两个解 > 5 V

## Slide 40
①
②
③
④
④ > 5 V

## Slide 41
①工作于饱和区

## Slide 42
②确保VD的上限不超过 VG + |VTH|

## Slide 43
IDP = IDN  I = 0  VO = 0
①
②假设工作在饱和区
③确认在饱和区

## Slide 44
① QP cut off
② VD < 0  比VG – VTH 要低  工作在非饱和区

## Slide 45
① QN cut off
② VD > 0  比VG + |VTH| 要高  工作在非饱和区

## Slide 46: 作业