## Slide 1: 电子电路基础
第三讲：电路分析的基本方法和定理~part2

## Slide 2: 电路分析的基本方法和定理
1.3.1 电容和电感（原理、符号及其特性定量描述）
2.4 储能元件电路的等效变换
2.4.1 电容的串联和并联
2.4.2 电感的串联和并联
2

## Slide 3: Capacitors and Inductors Chapter 6
电容、电感，及它们的串并联
6.1 Capacitors 电容
6.2 Series and Parallel Capacitors
6.3 Inductors 电感
6.4 Series and Parallel Inductors
3

## Slide 4: 6.1 Capacitors 电容
A capacitor is a passive (无源) element designed to store energy in its electric field. 储存电场能量
A capacitor consists of two conducting plates separated by an insulator (or dielectric).
4

## Slide 5
SMD
(surface mount device)
贴片电容
Through-hole
直插式电容
5

## Slide 6: 6.1 Capacitors (2)
Capacitance C is the ratio of the charge q on one plate of a capacitor to the voltage difference v between the two plates, measured in farads (F).
Where  is the permittivity of the dielectric material between the plates, A is the surface area of each plate, d is the distance between the plates.
Unit: F, pF (10–12), nF (10–9), and
and
F (10–6)
介电常数
平板面积
平板间距离
平板上的电荷量
电压
电容的定义：导板上的电荷和导板之间电势差的比值
6

## Slide 7: 6.1 Capacitors (3)
If i is flowing into the +v terminal of C
  电流从+端流入 充电Charging
  电流从+端流出 放电Discharging
电容也是基本的电路元件，我们需要熟悉流过它的电流和它两端电压之间的关系，就如熟悉电阻一样。The current-voltage relationship of capacitor according to above convention is ：电容的“电压-电流”关系
7

## Slide 8: 6.1 Capacitors (4)
The energy, w, stored in the capacitor is (电容存储的电能)：
电容的两个基本属性
  an open circuit to dc (dv/dt = 0). 直流开路
  its voltage cannot change abruptly. 电容两端电压不能突变，Why？
√
×
8

## Slide 9
9

## Slide 10
10

## Slide 11
11

## Slide 12
电容：直流开路
12

## Slide 13
电容的模型
理想电容器模型
考虑漏电时的电容器模型
高频时的电容器模型
C
＋
v
i
－
C
＋
－
R
C
＋
－
R
L

## Slide 14: 6.2 Series and Parallel Capacitors (1)
The equivalent capacitance of N parallel-connected capacitors is the sum of the individual capacitances.
14
电容并联：
电压相等，电流相加  C相加

## Slide 15: 6.2 Series and Parallel Capacitors (2)
The equivalent capacitance of N series-connected capacitors is the reciprocal of the sum of the reciprocals of the individual capacitances.
若N=2：
电容串联：
电流相等，电压相加 1/C相加  类似于电阻并联
15

## Slide 16
16

## Slide 17
串联电容的q相等
17
Q=CV, V之比等于1/C之比

## Slide 18: 6.3 Inductors 电感
An inductor is a passive element designed to store energy in its magnetic field. 储存磁能
An inductor consists of a coil of conducting wire.
磁导率
18

## Slide 19
19

## Slide 20: 6.3 Inductors (2)
电感也是基本的电路元件，我们需要熟悉流过它的电流和它两端电压之间的关系，就如熟悉电阻一样。 电感的“电压-电流”关系：
The unit of inductors is Henry (H), mH (10–3) and H (10–6).
20

## Slide 21: 6.3 Inductors (3)
The power stored by an inductor:
电感的两个基本属性：
①直流短路(di/dt = 0) ；②电流不能突变，Why？
√
×
21

## Slide 22
22

## Slide 23
23

## Slide 24
电容直流开路；电感直流短路
24

## Slide 25
电感的模型
＋
L
－
v(t)
R
C
工作频率很高的情况
理想电感
考虑内阻
L
＋
－
v(t)
R
i
+
－
v (t)
i
L

## Slide 26: 6.4 Series and Parallel Inductors (1)
The equivalent inductance of series-connected inductors is the sum of the individual inductances.
26
电感串联：
电流相等，电压相加  L相加

## Slide 27: 6.4 Series and Parallel Inductors (2)
The equivalent capacitance of parallel inductors is the reciprocal of the sum of the reciprocals of the individual inductances.
若N=2：
电感的串并联与电阻器的电阻值计算一样！
电感并联：
电压相等，电流相加  1/L 相加
27

## Slide 28
28

## Slide 29
29
电感：根据电压求电流，需要先求出各电感的初始电流值
i2(t) 也可以用i – i1(t) 获得

## Slide 30
30

## Slide 31: 小结
电感：直流短路，流过电感的电流不能突变
电容并联：C相加；电容串联：相当于电阻并联；
电感的串并联相当于电阻的串并联
电容，根据电流求电压，需要先求电容两端电压的初始值；
电感，根据电压求电流，需要先求流过电感的电流初始值；
31

## Slide 32: 作业
32

## Slide 33
电容串并联；串联电容的q相等

## Slide 34
电容直流开路；电感直流短路