## Slide 1: Chapter #2: Operational Amplifiers 运算放大器
from Microelectronic Circuits Text
by Sedra and Smith
Oxford Publishing

## Slide 2: 课程纲要
9. 理想运算放大器及其应用电路（建议4学时）
9.1 运算放大器基础
9.1.1 运算放大器的结构及其电路符号
9.1.2 运算放大器的理想模型
9.2 运算放大器基本应用电路
9.2.1 反相和同相接法电路
9.2.2 常用运算放大器应用电路（包括线性和非线性应用电路）
2

## Slide 3: Introduction
IN THIS CHAPTER YOU WILL LEARN
  The terminal characteristics of the ideal op-amp.理想运放的基本特性
  How to analyze circuits containing op-amps, resistors, and capacitors. 基本运放电路的分析
  How to use op-amps to design amplifiers having precise characteristics. 利用运放设计精确放大器
3

## Slide 4: Introduction
IN THIS CHAPTER YOU WILL LEARN
  How to design more sophisticated op-amp circuits, including summing amplifiers, instrumentation amplifiers, integrators, and differentiators.
  运放主要应用电路分析
4

## Slide 5: 2.1.1. The Op Amp Terminals
terminal #1 反相输入端
  inverting input
terminal #2 同相输入端
  non-inverting input
terminal #3 输出端
  output
terminal #4 供电电源（+）
  positive supply VCC
terminal #5 供电电源（-）
  negative supply VEE
从信号角度讲，op amp 是一个三端元件（1、2、3），4和5是供电。
Op amp 也是一个基本的 building block，就如R、L、C
“电压电流约束关系”：
Notes: A useful integrated circuit implementation of an almost idealized amplifier. Often
VCC = VEE for balance with respect to ground (important as it maintains symmetry when overdriven)
Some OpAmps also have differential outputs

## Slide 6
6

## Slide 7: 2.1.3. Differential & Common-Mode Signals
Q: How is common-mode input (vcmi) defined in terms of v1 and v2?
差分信号 & 共模信号
差分：vdi = v2 - v1
共模：vcmi = (v2 + v1 )/2
任意两个信号v1，v2，都可以分解成共模信号（vcmi） 与 差分信号（Vdi）的叠加
7

## Slide 8: 2.1.3. Differential & Common-Mode Signals
8
Notes: A good equivalent circuit as long as your system is balanced

## Slide 9: 2.1.2. Function and Characteristics of Ideal Op Amp
ideal input characteristic is infinite impedance
ideal output characteristic is zero impedance
differential gain (A) is infinite
common mode gain is zero
bandwidth gain is constant from dc to high frequencies
Q: But, is an amplifier with infinite gain of any use?
输入阻抗=∞
输出阻抗=0
差分电压增益=∞
带宽= ∞
理想运放不单独使用，输入输出需构成闭环再应用，所以A也称为开环增益（open-loop gain），相应的，构成闭环后的增益成为闭环增益（closed-loop gain）
了解理想运放的基本特性，就如需要了解RLC元件的基本特性一样
电压关系：
电流关系：i1=i2=0
9
共模电压增益=0
理想运放的等效电路

## Slide 10
简化 symbol，常用
10

## Slide 11: 2.1.2. Function and Characteristics of Ideal Op Amp
ideal gain: is defined below
ideal input characteristic: infinite impedance
ideal output characteristic: zero impedance
理想运放的特性：
①输入阻抗=∞； i1=i2=0 虚断
②输出阻抗=0；
③只放大输入差分信号；
④差分电压增益=∞； v1=v2 虚短
⑤带宽=∞
理想运放的等效电路
11
④
Notes: Idealized OpAmp:
Infinite input impedance (no source loading)
Extremely high gain (A – watch out for oscillation)
Zero output impedance (can deliver power to a load), but real OpAmps are not Zero (741 has 75 ohm Zout)
Differential input (high degree of “common mode” rejection)
Sometimes differential output

## Slide 12: 2.1.2. Function and Characteristics of Ideal Op-Amp
An amplifier’s input is composed of two components…
  differential input (vdfi) – is difference between inputs at non-inverting and inverting terminals
  common-mode input (vcmi) – is input present at both inverting and non-inverting terminals
Similarly, two components of gain exist…
  differential gain (A) – gain applied to differential input ONLY
  common-mode gain (Acm) – gain applied to common-mode input ONLY
运放的特性：
抑制共模信号、放大差分信号
运放的增益也可看成两部分构成：差分增益+共模增益
12
Notes: An OpAmp tries to reject the common-mode input while amplifying the differential input.

## Slide 13: 2.1.2. Function and Characteristics of Ideal Op Amp
This “Ideal” is only approached by IC op amps
Zi – usually high enough to ignore
Zo – often higher than needed – follow by a low output impedance stage (emitter-follower)
Acm – usually quite good
A – usually high enough when not asking for too much gain with feedback
BW – needs to be evaluated in use.
理想运放可以用集成运放（集成电路，而非分立元件实现运放）来近似实现
输入阻抗往往够高
输出阻抗往往不够低，需后接一级低输出阻抗的电路
共模增益往往够小
差分增益往往够高
需根据实际情况估算，≠∞
∞
0
0
∞
∞
13

## Slide 15: 2.2. The Inverting Configuration
Q: What are two basic closed-loop op-amp configurations which employ op-amp and resistors alone?
  A: 1) inverting and 2) non-inverting op amp
反相（倒相）接法
若仅可使用运放和电阻，那么有两种构成闭环的接法：①反相接法，输入在反相输入端；②同相接法，输入在同相输入端
15
Notes: Two of the three most used configurations

## Slide 16: 2.2. The Inverting Configuration
question: what are two basic closed-loop op amp configurations which employ op-amp and resistors alone?
  answer: inverting and non-inverting op amp
  note: here we examine the inverting type
source is applied to inverting input
non-inverting input is grounded
R2 facilitates “negative feedback”
R1 regulates level of this feedback
Figure 2.5: The inverting closed-loop configuration.
16
Notes: How can we calculate the gain?

## Slide 17: 2.2.1. Closed-Loop Gain
Q: How does one analyze closed-loop gain for inverting configuration of an ideal op-amp?
  step #1: Begin at the output terminal
  step #2: If vOut is finite, then differential input must equal 0
    virtual short circuit between v1 and v2
    virtual ground exists at v1
关键点：因为输出电压为有限值，所以输入必须为零（增益A为∞），也即 v2 = v1
1 和 2 之间电压相等，但实际物理上没有连接  “虚短”
2的电压碰巧是0V，所以1称为“虚拟地”
17
Notes: Step “2” is a deduced fact! – very clever

## Slide 18: 2.2.1. Closed-Loop Gain
step #3: Define current into inverting input (i1).
step #4: Determine where this current flows?
  refer to following slide…
18
Notes: Here we are using Node Equations

## Slide 19: 2.2. The Inverting Configuration
question: what are two basic closed-loop op amp configurations which employ op-amp and resistors alone?
  answer: inverting and non-inverting op-amp
  note: here we examine the inverting type
Figure 2.5: The inverting closed-loop configuration.
i1
i = 0
i1
19
Notes: Here we are using “Node equations” to solve for amplifier gain.
Note that V2 = V1 ! Why?
V1 is at a “virtual ground” due to the high gain (vo is finite)

## Slide 20: 2.2.1. Closed-Loop Gain
step #5: Define vOut in terms of current flowing across R2.
step #6: Substitute vin / R1 for i1.
note: this expression is one of the fundamentals of electronics
20
Notes: We had this result in Circuits!

## Slide 21: 2.2.1. Closed-Loop Gain
question: how will we…
  step #4: define vOut in terms of current flowing across R2
  step #5: substitute vin / R1 for i1.
Figure 2.6: Analysis of the inverting configuration. The circled numbers indicate the order of the analysis steps.
closed-loop gain G = -R2/R1
21

## Slide 22: 2.2.1. Effect of Finite Open-Loop Gain
Q: How does the gain expression change if open loop gain (A) is not assumed to be infinite?
  A: One must employ analysis similar to the previous, result is presented below…
ideal gain
non-ideal gain
若开环增益A≠∞，如何计算？
22
Notes: Seldom needed as the gain is very high

## Slide 23
23

## Slide 24: 2.2.1. Effect of Finite Open-Loop Gain
Q: Under what condition can G = -R2 / R1 be employed over the more complex expression?
  A: If 1 + (R2/R1) << A, then simpler expression may be used.
ideal gain
non-ideal gain
什么条件下G可近似等于 -R2/R1？

## Slide 25: Example 2.1: Simple Inverting Amplifier
Problem Statement: Consider an inverting configuration with R1 = 1kOhm and R2 = 100kOhm.
Q(a): Find the closed-loop gain (G) for the cases below. In each case, determine the percentage error in the magnitude of G relative to the ideal value.
  cases are A = 103, 104, 105…
  What is the voltage v1 that appears at the inverting input terminal when vIn = 0.1V.
Q(b): If the open loop gain (A) changes from 100k to 50k, what is percentage change in gain (G)?
25

## Slide 26
* Op amp 独自是不能用的，因为开环增益A为无穷大，必须外接电阻或电容等元件构成闭环反馈。Inverting configuration 是常见的一种构成闭环反馈的结构，其闭环电压增益仅与外接电阻有关。【trade-off：trade gain for accuracy】
26

## Slide 27: 2.2.3. Input and Output Resistances
Q: What is input resistance for inverting op-amp? How is it defined mathematically?
  A: R1 (refer to math below)
Q: What does this say?
  A: That, for the combination of ideal op-amp and external resistors, input resistance will be finite…
assumes ideal op-amp
输入电阻 & 输出电阻
关键点：V1=V2=0；
27
Notes: Input resistance is determined by R1
Take this into account in your designs or use a “Buffer amp”

## Slide 28
输出电阻呢？
0
理想op amp 输出是一个理想电压源，内阻为零，外接反馈电阻不影响输出电阻
28

## Slide 29: 思考
理想的电压电压放大器，要求输入阻抗尽可能大  输入阻抗（R1）要尽可能大；
大的增益（-R2/R1）  R2的值会大得不切实际，如几MΩ等  只能牺牲R1，取较小的R1值
因此，常规反相连接运放电路存在输入阻抗较低的缺点
29

## Slide 30: Example 2.2: Another Inverting Op-Amp
Problem Statement: Consider the circuit below...
Q(a): Derive an expression for the closed-loop gain vOut/vIn of this circuit.
Q(b): Use this circuit to design an inverting amplifier with gain of 100 and input resistance of 1Mohm.
  Assume that one cannot use any resistor with resistance larger than 1Mohm.
Q(c): Compare your design with that based on traditional inverting configuration.
Figure 2.8: Circuit for Example 2.2. The circled numbers indicate the sequence of the steps in the analysis.
30

## Slide 31
①
②
④
⑤
⑥
⑦
⑧
R1=1MΩ  R2=1MΩ R4=1MΩ  R3用来实现增益 10.2kΩ
传统电路实现100的增益，R2=100MΩ
31

## Slide 32: Example 2.2: Another Inverting Op-Amp
The largest resistor on may choose is 1Mohm
Q: Where does one begin (in choosing the resistor values)? Which resistor would you define to be 1Mohm?
  A: The input resistance (R1) should be set as high as possible, therefore 1Mohm
Q: What other resistor values should be defined?
  A: R2 = 1Mohm, R4 = 1Mohm, R3 = 10.2kohm
PART B: Use this circuit to design an inverting amplifier with gain of 100 and input resistance of 1Mohm. Assume that one cannot use any resistor with resistance larger than 1Mohm.
Figure 2.9: A current amplifier based on the circuit of Fig. 2.8. The amplifier delivers its output current to R4. It has a current gain of (1 + R2 /R3)
R2、R3是并联的  若R3为R2的1/k，则i3是i2的k倍  i4是i2(i1)的k+1倍
换个角度思考：
【Insight】
32

## Slide 33
33

## Slide 34: 2.2.4. An Important Application – The Weighted Summer
weighted summer - is a closed-loop amplifier configuration which provides an output voltage which is weighted sum of the inputs.
Figure 2.10: A weighted summer.
加法器
34
Notes: An important configuration

## Slide 35: 2.2.4. An Important Application – The Weighted Summer
weighted summer - is a closed-loop amplifier configuration which provides an output voltage which is weighted sum of the inputs.
Figure 2.10: A weighted summer.
vIn1
vIn2
vIn3
vOut
Rf
RIn1
RIn2
RIn3
vOut = -[ (Rf./RIn1)vIn1 + (Rf./RIn2)vIn2 + (Rf./RIn3)vIn3 + … ]
35

## Slide 36
实现加减法
36

## Slide 37
37

## Slide 38: 2.3. The Non-Inverting Configuration
non-inverting op-amp configuration – is one which utilizes external resistances (like the previous) to effect voltage gain. However, the polarity / phase of the output is same as input.
同相接法
38

## Slide 39: 2.3. The Non-Inverting Configuration
Figure 2.12: The non-inverting configuration.
source is applied to non-inverting input
inverting input is grounded through R1
R1 and R2 act as voltage divider, regulating negative feedback to the inverting input
node #1
node #2
不管是inverting，还是non-inverting，反馈电阻都是接到“➖”端
39

## Slide 40
①
②
③
④
⑤
⑥
可以看成分压
40

## Slide 41
若开环增益A不是无穷大，则如何计算？
v2-v1=vo/A
同样，输入阻抗为∞，输出阻抗为0
41

## Slide 42: Characteristics of Non-Inverting Op-Amp Configuration
42
Notes: Note the 1+ in the Gain!

## Slide 43: Configuration and Characteristics of Buffer / Voltage-Follower Op-Amp Configuration
Figure 2.14: (a) The unity-gain buffer or follower amplifier. (b) Its equivalent circuit model.
Buffer amp: 提供高输入阻抗、低输出阻抗，增益非主要考虑因素
43
Notes: This is a useful configuration to “buffer” sub-circuits.

## Slide 44: Configuration and Characteristics of Buffer / Voltage-Follower Op-Amp Configuration
Figure 2.14: (a) The unity-gain buffer or follower amplifier. (b) Its equivalent circuit model.
Main point? For the buffer amp, output voltage is equal (in both magnitude and phase) to the input source. However, any current supplied to the load is drawn from amplifier supplies (VCC, VEE) and not the input source (vI).
44

## Slide 45
对v1，v2应用叠加原理
45

## Slide 46
46

## Slide 47: 2.4. Difference Amplifiers 差分放大器
difference amplifier – is a closed-loop configuration which responds to the difference between two signals applied at its input and ideally rejects signals that are common to the two.
  Ideally, the amp will amplify only the differential signal (vdfi) and reject completely the common-mode input signal (vcmi). However, a practical circuit will behave as below…
理想差分放大器，只放大输入的差分信号，对输入共模信号的增益为零
但实际上，会存在较小的共模增益
47

## Slide 48: 2.4. Difference Amplifiers
differential gain
differential input
common-mode input
common-mode gain
48

## Slide 49: 2.4. Difference Amplifiers
common-mode rejection ratio (CMRR) – is the degree to which a differential amplifier “rejects” the common-mode input.
  Ideally, CMRR = infinity…
共模抑制比
49

## Slide 50: 2.4. Difference Amplifiers
Figure 2.15: Representing the input signals to a differential amplifier in terms of their differential and common-mode components.
50

## Slide 51: 2.4. Difference Amplifiers
Q: The op amp itself is differential in nature, why cannot it be used by itself? 运放本身就是差分输入的，为何不能直接用作差分放大器？
  A: It has an infinite gain, and therefore cannot be used by itself. One must devise a closed-loop configuration which facilitates this operation.
  运放增益太大，且不稳定、不精确（一个很大的增益是做不到稳定和精确的）
  我们需要牺牲增益，来换取稳定性和精确性（trade-off，折衷）
51

## Slide 52: 【Insight】如何构建一个差分放大器？
将noninverting configuration的输入适当衰减，使其总的增益等于R2/R1，则可构成一个差分放大器
52

## Slide 53: 2.4. Difference Amplifiers
Figure 2.16: A difference amplifier.
利用叠加原理计算
53

## Slide 54: 2.4.1. A Single Op-Amp Difference Amp
Q: What are the characteristics of the difference amplifier?
  A: Refer to following equations…
平衡条件
54
Notes: Note: the resistors must be matched to maintain “balance”!
R1 = R3
R2 = R4

## Slide 55: 共模输入情况
①
②
③
④
⑤
①
②
③
④
⑤
平衡时，Acm=0；若不平衡，Acm≠0
55

## Slide 56: 输入阻抗
① Rid 差分输入阻抗
② 考虑平衡情况
存在的缺点：
差分放大器需要提供较大差分增益（R2/R1）  R1要小  输入阻抗变小！
如何解决这一缺点？
56

## Slide 57
57

## Slide 58: A Shift in Notation
Before this point…
  The parameter A is used to represent open-loop gain of an op amp.
  The parameter G is used to represent ideal / non-ideal closed-loop gain of an op amp.
After this point…
  The parameter A is used to represent ideal gain of an op amp in a given closed-loop configuration.
  The parameter G is not used.
A代表理想运放的闭环增益
58

## Slide 59: 2.4.2. The Instrumentation Amplifier 仪表放大器
Q: What is one problem associated with the difference amplifier? 差分放大器存在的缺点
  A: Low input impedance. 输入阻抗低
Q: And, what does this mean practically? 有什么影响
  A: That source impedance will have an effect on gain. 输入端分压衰减  施加于放大器输入端的有效信号电压降低
Q: What is the solution? 解决方法
  A: Placement of two buffers at the input terminals, amplifiers which transmit the voltage level but draw minimal current. 在输入端插入buffer amp，提高Rin
59

## Slide 60: 2.4.2. The Instrumentation Amplifier
Q: However, can one get “more” from these amps than simply impedance matching?
  A: Yes, maybe additional voltage gain???
  在插入buffer amp，以提高输入阻抗的同时，还可以获得额外的增益
60

## Slide 61: 2.4.2. The Instrumentation Amplifier
question: however, can we get “more” from these amps than simply impedance matching?
  answer: yes, maybe additional voltage gain???
Figure 2.20: A popular circuit for an instrumentation amplifier.
stage #1
non-inverting op amp (A1)
non-inverting op amp (A2)
stage #2
difference op amp (A3)
vo1 = (1 + R2/R1)vIn
vOut = (R4/R3)vdfi
61

## Slide 62: 2.4.2. The Instrumentation Amplifier
Q: However, can one get “more” from these amps than simply impedance matching?
  A: Yes, maybe additional voltage gain???
additional voltage gain
62

## Slide 63: 2.4.2. The Instrumentation Amplifier
Advantages优点 of instrumentation amp
  very high input resistance 输入阻抗很大
  high differential gain 差分增益变大
  symmetric gain (assuming that A1 and A2 are matched)
Disadvantages缺点 of instrumentation amp
  ADi and ACm are equal in first stage – meaning that the common-mode and differential inputs are amplified with equal gain… 第一级放大器对差分输入和共模输入进行了同样程度的放大！  ①信号幅度过大容易使运放饱和；②第二级有更大的CMRR压力
63

## Slide 64: What is problem with ACm = A?
differential gain >> common-mode gain
differential gain = common-mode gain
vIn1
vIn2
vIn1
vIn2
A = 10 x 25
A = 10
A = 25
Case 1: 没有共模增益时
Case 2: 当第一级有共模增益时
64

## Slide 65: differential gain >> common-mode gain
vIn1 = 10.02V
vIn2 = 10.03V
A = 10 x 25
vOut= 250 x (10.03-10.02)V
vOut = 2.5V no problem!!!
65

## Slide 66: differential gain = common-mode gain
A = 10
A = 25
vIn1 = 10.02V
vIn2 = 10.03V
vOut1= 10 x 10.02 = 15V saturation
vOut2= 10 x 10.03 = 15V saturation
vOut= 25 x (15-15)V
vOut = 0V problem!!!
供电电源 ±15 V，限制了电路中最大允许的电压范围
66

## Slide 67: 2.4.2. The Instrumentation Amplifier
advantages of instru. amp
  very high input resistance
  high differential gain
  symmetric gain (assuming that A1 and A2 are matched)
disadvantages of instrumentation amp
  ADi and ACm are equal in first stage – meaning that the common-mode and differential inputs are amplified with equal gain…
  need for matching – if two op amps which comprise stage #1 are not perfectly matched, one will see unintended effects 如果第一级不完美匹配，那么将会对第二级的输入引入额外的差分信号
67

## Slide 68: 2.4.2. The Instrumentation Amplifier
Q: How can one fix this (alleviate these disadvantages)?
  A: Disconnect the two resistors (R1) connected to node X from ground, making the configuration “floating” in nature…
  A: Refer to following slide…
68

## Slide 69: 2.4.2. The Instrumentation Amplifier
Figure 2.20: A popular circuit for an instrumentation amplifier. (b) The circuit in (a) with the connection between node X and ground removed and the two resistors R1 and R1 lumped together. This simple wiring change dramatically improves performance.
仅仅是简单地将X点的接地去掉，就能解决上述问题！【巧妙的工程实现】
69
Notes: A useful configuration

## Slide 70: 2.4.2. The Instrumentation Amplifier
Q: How can one analyze this circuit?
70
Notes: Again – maintain balance!

## Slide 71
①
①
②
③
④
④
⑤
⑥
共模信号输入呢？
流经2R1的电流为零  流经R2的电流也为零  A1、A2的输出电压即VI1、VI2
 第一级没有对共模信号进行放大！
对比原先电压
对比原先电压
71

## Slide 72
第一级实现增益
第一级实现共模抑制
把第二级增益设定为1
72

## Slide 73
73
10 kW 是常用电阻

## Slide 74: 2.5. Integrators and Differentiators 积分电路 & 微分电路
integrator / differentiator amplifier – is one which outputs an integral or derivative of the input signal.
用模拟电路来实现积分、微分、加减法运算，这就是“运算”放大器名称的由来
In earlier days we use Analog computers using adders, integrators and multipliers.
Now Simulink (in MatLab) simulates an Analog computer using a digital computer.
74

## Slide 75: 2.5.1. The Inverting Configuration with General Impedances
Q: Does the transfer function for the inverting op amp change if the feedback and input impedances are not purely resistive? 在反相接法中，若将电阻换成更普遍的阻抗，会如何？
  A: 增益形式不变，只需将R替换成Z
75

## Slide 76: 一阶电路特性回顾
s = jw
76
传递函数标准形式
低通STC
高通STC

## Slide 77: Example 2.4: Other Op-Amp Configurations 例题
考虑右边的电路
Q(a): Derive an expression for the transfer function vOut / vIn. 求传输函数的表达式
Q(b): Show that the transfer function is of a low-pass STC circuit. 验证传输函数是低通STC电路
Q(c): By expressing the transfer function in standard form of Table 1.2, find the dc-gain and 3dB frequency.
用STC的标准表达式，计算直流增益和3dB频率
77

## Slide 78: Example 2.4: Other Op-Amp Configurations
Figure 2.23: Circuit for Example 2.4.
78

## Slide 79: 2.5.2. The Inverting Integrator 反相积分电路
Q: How can inverting op-amp be adapted to perform integration? 如何用反相接法的运放实现积分功能
  A: Utilization of capacitor as feedback impedance.
  利用电容作为反馈阻抗
79

## Slide 80
①
②
③
④
该结构的积分电路也被称为
Miller积分器
时域
频域
（积分器频率）
-20 dB/十倍频
= -6 dB/两倍频
波特图
80
CR称为积分器的时间常数

## Slide 81: 2.5.2. The Inverting Integrator
Q: What is the problem with this configuration (related to dc gain)? 存在的问题
  A: At dc frequency (w = 0), gain is infinite 低频增益∞
  Gain = 1 / (w.R1CF)
Q: Solution? 解决的办法
  A: By placing a very large resistor in parallel with the capacitor, negative feedback is employed to make dc gain “finite.” 用一个大电阻并联反馈电容
81

## Slide 82: 2.5.2. The Inverting Integrator
Figure 2.25: The Miller integrator with a large resistance RF connected in parallel with C in order to provide negative feedback and hence finite gain at dc.
但引入RF后，积分特性变得不完美了！
因此，RF的取值需在dc性能和信号积分性能之间取trade-off
就是前面例题2.4的情况
82

## Slide 83
假设电容初始电压为0
1. 没有 RF 的情况
t 的单位是 ms
1 V 电压产生 0.1 mA 电流，对 C 进行充电
83
时间常数

## Slide 84
假设电容初始电压为0
2. 有 RF 的情况
1 V 电压产生 0.1 mA 电流，流入 C 和 RF 网络
C的初始电压 0，稳态电压 0.1mA x RF = 100 V，时间常数 t =RF x C = 10 ms
84
从方波产生三角波

## Slide 85: 2.5.3. The Op-Amp Differentiator 微分电路
Q: How can one adapt integrator to perform differentiation? 如何构建微分电路呢？
  A: Interchange locations of resistors and capacitors.
  将积分电路的R和C交换，即可实现微分电路
Figure 2.27: A differentiator.
85

## Slide 86: 2.5.3. The Op-Amp Differentiator
86
高频时，C阻抗很小，增益很大，输出容易饱和。因此常常在输入端与C串联一个电阻，以抑制高频增益

## Slide 87: 2.5.3. The Op-Amp Differentiator
filtering characteristic is high pass filter
magnitude of transfer function is |VOut / VIn| = wRFC1
phase of transfer function is f = -90O
differentiator time-constant is frequency at which unity gain occurs and defined as w = 1 / RFC1
Q: What is the problem with differentiator?
  A: Differentiator acts as noise amplifier, exhibiting large changes in output from small (but fast) changes in input. As such, it is rarely used in practice.
  输入有突变，则输出无穷大
87
Notes: Again you can parallel the input capacitor to limit the noise problem.

## Slide 88: 补充说明
Op amp 输入端电压相等只是在开环增益为无穷大的理想情况下成立，若开环增益为有限值，输入端电压差为“输出/开环增益”

## Slide 89: 补充说明
Vin2 看作 Vout 的分压

## Slide 90: 小结
运放的“电压电流约束关系”
理想运放的特性
输入阻抗无穷大
输出阻抗为0 (输出是理想电压源)
开环增益 A 无穷大
带宽无穷大
共模增益为0
90

## Slide 91
Inverting Configuration
Noninverting Configuration
91

## Slide 92
差分放大器
仪表放大器
92

## Slide 93
应用 1：加法
应用2：Buffer
93

## Slide 94
应用 3：积分
应用4：微分
94

## Slide 95: 作业
95

## Slide 96
10 kW 是常用电阻